## Slide 1: Full Adder Design Using Reversible Logic with Different Tools for Low Power VLSI A PROJECT REPORT Submitted by Caprio Mistry Ashis Paul Sugata Roy Chowdhury Swarnali Mitra in partial fulfillment for the award of the degree of BACHELOR OF TECHNOLOGY in Department of Electronics & communication Engineering

## Slide 2: BRAINWARE UNIVERSITY 398, Ramkrishnapur Road, Barasat, North 24 Parganas, Kolkata - 700 125 Electronics & communication Engineering
BONAFIDE CERTIFICATE
Certified that this project report “Full Adder Design Using Reversible Logic with Different Tools for Low Power VLSI” is the bonafide work of “Caprio Mistry, Ashis Paul, Sugata Roy Chowdhury, Swarnali Mitra” who carried out the project work under my supervision.
Dr. Angshuman Majumder
HEAD OF THE DEPARTMENT
Electronics and Communication Engineering
Brainware University
398, Ramkrishnapur Road, Barasat,
North 24 Parganas, Kolkata-700125
Dr. Debasis Mukherjee
SUPERVISOR
Associate Professor.

## Slide 3: Index
Abstract
Introduction
Need for Reversible Computing
Technical Requirement for Reversible Computing
Literature Review
VLSI Technology’s Advantages
Objective and Planning
Requirement Analysis
Tools required and used
System Flow
Proposed Design
Experimental Result
Future Scope
Conclusion
References and Sources

## Slide 4: Abstract
In this work we propose a study to the logic design synthesis of different circuit by using reversible computing. This study is based on the use of full adder circuit using reversible logic synthesis. The idea is designing an adder circuit with low power dissipation and low power consumption. Among the properties of reversible gate, we have a minimum of input constant number of gate and number of garbage output. Garbage output are those output which is not using for any consumption.
Full adder cell is one of the most frequently used digital circuit component in arithmetic logic unit (ALU) and it is the essential functional unit of all computational circuit. Till now lots of improvement has been done in this area to refine the architecture and performance of full adder circuit design. In this project, designs of novel full adder cell at 90nm CMOS technology are implemented by using CMOS transistors along with the existing full adder cell using reversible computing.

## Slide 5: Introduction
Scientist R. Landauer proved in 1961 that energy dissipation is caused by the loss of each bit of information. The amount of energy dissipated for one bit of information loss is KTln2 joules, where K is the Boltzmann's constant and T is the operating temperature. At ambient temperature, the heat released by the loss of one bit of information is extremely tiny, but in the case of high computational tasks, when the number of bits is greater, the heat dissipated by them is so significant that it impacts performance and reduces component lifespan. C. H. Bennett demonstrated in 1973 that reversible logic gates must be used in a logic circuit to prevent KTln2 energy loss.

## Slide 6: What is Reversible Computing?
Reversible computing refers to any type of computation in which the computational process is time-reversible to some extent. A required criterion for reversibility in a model of computation that employs deterministic transitions from one state of the abstract machine to another is that the mapping between states to their successors be one-to-one. Reversible computing is a type of unusual computing.

## Slide 7: Need for Reversible Computing
As we pack more and more logic elements into smaller and smaller volumes and clock them at higher and higher frequencies, we dissipate more and more heat. This creates at least three problems:
Energy costs money.
Portable systems exhaust their batteries.
Systems overheat.
I/O Bit Loss.
Since Reversible Computing uses output bits as the source for input bits without any kind of amplification and repetition peripheral module, a lot of the problems discussed above are eradicated. Thus we need Reversible Computing.

## Slide 8: Technical Requirement for Reversible Computing

## Slide 9: Literature Review
In this work, we offer a study of logic design synthesis of various circuits utilizing reversible computing. This research is based on the utilization of a complete adder circuit with reversible logic synthesis. The objective is to create an adder circuit with minimal power dissipation and usage. We have a minimum of input constant number of gate and number of garbage output among the reversible gate attributes. Garbage output is any output that is not being consumed.
Full adder cells are one of the most often utilized digital circuit components in arithmetic logic units (ALUs), and they are the fundamental functional unit of all computational circuits. Power consumption and speed have emerged as important factors in the design of devices such as laptops, tablets, mobile phones, notebook computers, and a range of other personal communication devices. Power consumption is crucial in VLSI technology.
More power consumption results in increased heating, which affects battery life and needs the usage of a cooling fan to keep the circuitry cool. As a result, power consumption has an impact on battery life as well as overall system cost. The majority of digital communication devices and the devices listed above are used in applications such as digital signal processing, image and video processing, and microcontrollers, and these applications require various arithmetic and logic operations to perform addition, subtraction, multiplication, and so on. Internally, all of these operations, such as addition, subtraction, and multiplication, may be performed.

## Slide 10: VLSI Technology’s Advantages
Circuits have been made smaller.
Devices have become more cost-effective.
In terms of circuit operating speed, the performance has improved.
When compared to separate components, it consumes less energy.
Devices that are more dependable.

## Slide 11: Objective and Planning
To design, simulate and synthesize a full adder circuit with implementing the concept of reversible computing. Nanotechnology should enable us to construct mole amounts of logic components. Unless the energy dissipation per logic operation is decreased to less than petajoules, the raw cost of power may become prohibitive, and the system may soon overheat.

## Slide 12: Requirement Analysis
Low-Power VLSI: Reversible computing spans computational models that are both forward and backward deterministic. These models have applications in program inversion and bidirectional computing, and are also interesting as a study of theoretical properties. A reversible computation does, thus, not have to use energy, though this is impossible to avoid in practice, due to the way computers are build. It is, however, not always obvious how to implement reversible computing systems. The restriction to avoid information loss imposes new design criteria that need to be incorporated into the design; criteria that do not follow directly from conventional models.
Over-heating: Whenever we use any handheld device like our smartphones, laptops or computers, the logic gates which are designed using the transistors start to work. The use of transistors for designing the logic gates is as fast as switches. But the debating point is about the heating of the devices. We all face the fact that our processors and mobile devices discharge lots of heat. The reason behind it is the increase of transistors on-chip (TOC).
I/O Bit Loss: A reversible circuit has exactly as many outputs as inputs. Each input can be reconstructed from the output; no bits are lost but in conventional logics cannot reconstruct the input from the output, so reversible circuits will not give off heat from bit loss.

## Slide 13: Tools required and used
DSCH( National Instruments Corps.)
Microwind 3.1 (National Instruments Corps.)

## Slide 14: System Flow

## Slide 15: Proposed Design: Gate Level Designs using DSCH
Feynman Gate(FG)
Feynman gate is a 2 inputs 2 outputs (2x2) reversible gate. Another name for Feynman gate is Controlled NOT gate having the mapping (A, B) to (P=A, Q=A⊕B) where A, B are the inputs and P, Q are the outputs, respectively. This gate is useful for copying the required outputs. Therefore, it can be known as a copying gate. It has a quantum cost of one. Its logic circuit is shown in below.

## Slide 16: Proposed Design: Gate Level Designs using DSCH (contd.)
Fredkin Gate(FRG)
Fredkin gate is a 3 inputs 3 outputs (3x3) reversible gate having the mapping (A, B, C) to (P=A, Q=A’B⊕AC, R=AB⊕A’C), where A, B, C are the inputs and P, Q, R are the outputs, respectively. It is also known as a Controlled Permutation gate. It has a quantum cost of five. Its logic circuit is shown in below.

## Slide 17: Proposed Design: Gate Level Designs using DSCH (contd.)
Toffoli Gate(TG)
Toffoli Gate is a 3 inputs 3 outputs (3x3) reversible gate having the mapping (A, B, C) to (P=A, Q=B, R=A.B⊕C). The other name for Toffoli gate is controlled controlled-NOT gate. It has a quantum cost of five. Its logic circuit is shown in below.

## Slide 18: Proposed Design: Symbol level IC design for Full adder circuit using reversible gates with DSCH

## Slide 19: Proposed Design: Physical design with CMOS 90 nm Technology with reversible logic using Microwind (with corresponding Verilog code)
module FULLADDER2(A,B,C,Sum,Carry);
input A,B,Carry;
wire w16,w17,w18,w19, w20, w21, w22;
and #(15) sub_3(w16, w2, A);
xor #(36) sub_4(w3, w16, vss);
and #(15) sub_6(w18, w6, w17);
not #(23) sub_7(w17, w3);
and #(15) sub_8(w19, vdd, w3);
or #(15) sub_9(Carry, w18, w19);
and #(15) sub_10(w20, w6, w3);
or #(8) sub_11(w9, w20, w21);
and #(15) sub_12(w21, vdd, w16);
and #(15) sub_15(w22, C, B);
xor #(22) sub_16(w6, w22, vss);
xor #(22) sub_18(w2, w12, w13);
xor #(15) sub_20(Sum, w4, w5);
endmodule

## Slide 20: Experimental Result
Voltage->
Time->
From Physical Design cMOS Full Adder Circuit Operation

## Slide 21: Experimental Result
Sum= Light Blue
Carry= Purple
Voltage->
Time->
Output Trigger of Sum and Carry bits

## Slide 22
Future Scope
Reversible engineering has been one of the thrust areas ensuring that continual process of the innovation trends that explore and sustain the resources of the nature. This reversible engineering is used in many fields like quantum computing, low power CMOS design, nanotechnology, optical information processing, digital signal processing, cryptography, etc. These are the digital domain implementations of Reversible and Fault-Tolerant logic gates. Any arbitrary Boolean function can be synthesized by using the proposed parity preserving reversible gates. Not only the possibility of detecting errors is induced inherently in the proposed high-speed adders at their output side but also it allows any fault that affects no more than a single signal that is detectable. The fault tolerant reversible full adder circuits are realized by using two IG gates only. The derived fault tolerant full adder is used for designing other arithmetic- logic circuit by using it as fundamental building block. The proposed reversible gate is designed to have less hardware complexity and efficiency in terms of gate count, garbage outputs and constant input. In this paper, we design BCD adder using carry select logic, Carry-select and Bypass adders using FG gates, and newly designed TG gates.

## Slide 23: Conclusion
The proposed parity preserving reversible New TG gate is better than the existing reversible gates in terms of hardware complexity, gate count, garbage outputs, unit delay and constant inputs. Finally, this paper presents a novel implementation and realization of fault tolerant reversible circuits and demonstrates its superiority than the existing designs in terms of computational complexity. All the circuits are synthesized and verified using DSCH & Microwind software tool from National Instruments corps.

## Slide 24: References and Sources
Shukla, Neeraj & Birla, Shilpi & Kumar, Rakesh, & Mukherjee, Debasis. (2010). Analysis and Simulation of a Low Leakage Conventional SRAM Memory Cell at Deep Sub-micron Level. 70. 595-597. 10.1007/978-3-642-12214-9_108.
Mukherjee, Debasis. (2010). Analysis and Simulation of a Low Leakage Conventional SRAM Memory Cell at Deep Sub-Micron Level.
Bhattacharya, Soham & Goswami, Sourav & Sen, Anindya. (2020). Design of Complex Adders and Parity Generators Using Reversible Gates. 9. 83-88. 10.5281/zenodo.5555050
Bhattacharya, Soham & Sen, Anindya. (2021). A Review on Reversible Computing and it's applications on combinational circuits. 9. 9. 10.30534/ijeter/2021/28962021.

## Slide 25: Thank you